Practice for all formulas

In the table below fill in the appropriate triangle(s) used and give the unit for each variable.

| Voltage | Power | Energy - 2 formulas |
| --- | --- | --- |

Convert the following time units:

Minutes to seconds___________		W to kW	_________________

J to kJ		          ____________		J to kWh ______________________

Seconds to hours____________		Seconds to minutes _____________

Hours to seconds ____________

Using the above formulas and conversions, solve the following problems. Show all work.

- What is the current intensity of a circuit with a resistance of 25 Ω and a potential difference of 25 V?

- What is the resistance of a circuit with a current intensity of 4 A and a potential difference of 50 V?

- A radio is on for 3 hours and has 400 W of power. What is the energy in kWh?

- How much time elapsed in hours if a TV used 550 000 J of energy and needs 400 W of power?

- If a TV used 700 000 J of energy and 100 W of power. How many hours did you watch TV for?

- The circuit diagram shown below represents a heater with a resistance of 12 Ω through which flows a current of 10 A.  This heater is connected to a power source of 120 volts.  The heater was used for 20 minutes.

How much electric energy did the heater use?

- 14 400 J	B) 24 000 J	C) 28 800 J	D) 1 440 000 J

- The following graph shows the variation of the voltage across the terminals of a ceramic element as a function of the intensity of the current passing through it.

What power is dissipated when this ceramic element is connected to a voltage of 5.0 V?

- 20 W		B) 10.0 W		C) 5.0 W		D) 2.5 W

- What is the potential difference when a microwave runs on 1.2 A and uses 300 W of power

- What is the power needed for a compute to be on for 4 hours which produced 5 000 J of energy?

- What is the voltage of a circuit if it is using a 10 Ω resistor and 0.5 A of current?

- What is the voltage if an overhead 300 W of power and 1.5 A?

- The rating plate below indicates the characteristics of Jasmine’s hair dryer

MODEL – J45-TX2 110 V 1200 W

Jasmine took 15 minutes to dry her hair. How much electrical energy did Jasmine use to dry her hair?

- 300 J		B) 18 000 J		C) 99 000 J		D) 1 080 000 J

- What was the potential difference of a computer that used 55 000 J of energy when it was on for 2 hours and had 1.2 A?

- How much time passed in minutes when a computer did 700 000 J of work and had 550 W of power?

- What was the current intensity of a clock radio that used 50 000 J of energy when it was on for 5 hours and had 210 V?

- What was the current intensity of a clock radio if it used 100 V and a 100 Ω resistor?

- What is the resistance of a resistor if it uses 200 V and 5 A of current?

- What is the power in kW when a dishwasher used 20 V and 2.5 A?

- Wires create resistance to the flow of an electric current. This means that there is a drop in the voltage and that the wire heats up. An electrical circuit consists of a power source, an electrical device and 100 m of wire, as shown in the diagram below.

In this circuit, when the current intensity is 4 A, the maximum voltage drop due to the resistance of the wire is 1.32 V. What resistance value in the wire causes this voltage drop?

- 0.053 Ω		B) 0.33 Ω		C) 3.03 Ω		D) 5.28 Ω

- How much time elapsed in hours if a TV used 50 000 J of energy and needs 40 W of power?

- A hairdryer is on for 15 minutes and uses 220 V and 5.5 A how much energy will be used in kWh?

- What is the potential difference of a circuit if it has a 6.5 Ω resistor and 3.0 A?

- What is the resistance of a resistor if the power supply is set at 8 V and the current intensity is 2 A?

- An appliance is on for 90 minutes and uses 400 W of power how much energy will be used in J?

- How much time elapsed in minutes if a TV used 55 000 J of energy and needs 150 W of power?